## Slide 1
Drinking Water Safety & Security Planning
Part 2 Implementing DWSSP
Water Safety – Drinking Water Safety Planning
DWSSP Programme

## Slide 2
Imagine this community
Steady stream source
Good storage capacity
Each home has a tap
Each person has 100 litres per day
Water looks and tastes clean
What could possibly go wrong?
WaterAid (2013) Gravity-fed scheme – Tech brief. WaterAid, London.
Why Drinking Water Safety Planning?

## Slide 3
Well, the following could……
Drought hits hard
Storage Tank gets blown over in a storm
Water pressure drops
Population increases
Water becomes contaminated from a farm upstream
We look at Risks to minimise things going wrong!!!!
WaterAid (2013) Gravity-fed scheme – Tech brief. WaterAid, London.
Why Drinking Water Safety Planning?

## Slide 4
“The most effective means of consistently ensuring the safety of a drinking-water supply………
is through the use of a comprehensive risk assessment and risk management……..
approach that encompasses all steps in the water supply from catchment to consumer.”
DRINKING WATER SAFETY PLANNING
PREVENTING CONTAMINATION OF THE DRINKING WATER SUPPLY AND MANAGING RISKS
DWSP is Risk Management for Water Supplies

## Slide 5
Risk Management is a Process of:
Identifying Risk
Assessing and Prioritising Risk
Planning to Minimise Risk
What is Risk Management?

## Slide 6
Risk is made up of many things
Hazards
Control Measures
Sources of danger
Stops Hazards causing harm
HAZARD
Drinking Water Supply
Control Measure
Control Measure
Control Measure
What is Risk?

## Slide 7
Risk is the likelihood (or chance) of a hazard causing harm
Hazard
Control Measure
Hazard
Hazard
Hazard
Hazard
Hazard
Hazard
Hazard
Control Measure
HIGH RISK
Hazard
Control Measure
Hazard
Control Measure
LOW RISK
Control Measure
Control Measure
Control Measure
Control Measure
What is Risk?

## Slide 8
A simple risk assessment can boil down to only a few questions:
What can go wrong/cause harm?
What is the chance of it happening? How bad?
How can we minimise the chance of it happening?
Hazard Identification
Risk Analysis
Risk Management
Steps in a Risk Assessment

## Slide 9
Risk Assessment Example

## Slide 10
Risk Assessment Example

## Slide 11
What do you think can go wrong in a Drinking Water Supply?
Split into groups and discuss
Present back to group what you think can go wrong with Drinking Water
Hazard Identification – Exercise

## Slide 12
A. Identify area of the system
B. Understand what can go wrong
C. List the events that could lead to this
D. For each event, identify the risk factors
E. Then identify the CURRENT control measures
F. Evaluate the Risk of the event occurring
G. Plan to minimise the event occurring
A
B
C
D
E
F
G
Risk Assessment Steps for DWSP

## Slide 13
Catchment / Source
Treatment
Storage and Distribution
Consumer
A. Identify the area of the system

## Slide 14
There are 4 main problems we encounter with the provision of drinking water: What are they?
Bacteria Contamination
Chemical Contamination
Aesthetic (Unpleasant to Drink)
No Water Available
B. What can go wrong with drinking water?

## Slide 15
The main events that cause problems include:
Bacteria enters Drinking Water Supply
Chemicals enters Drinking Water Supply
Dirt/Soil/Solids enter the Drinking Water Supply
Drinking Water Supply flow is uncontrolled
Disaster or Climate Change effects including:
Drought
Flooding (Fresh or Salt Water)
Storm Damage
Earthquake
C. What events cause problems?

## Slide 16
Water Source | Water Distribution System
Bacteria enters Drinking Water Supply
Toilets and Animals Near Water
Dirt or Rubbish
Animal Access
Cracks and Leaks – Ingress
D. What are the Risk Factors for each event?

## Slide 17
Water Source | Water Distribution System
Chemicals enters Drinking Water Supply
Farming/ Pesticides
Waste Water Output
Corrosion
D. What are the Risk Factors for each event?

## Slide 18
Water Source | Water Distribution System
Dirt/Soil/Solids enter the Drinking Water Supply
Soil Erosion/ Surface Runoff
Unconsolidated Soil
Leaking Pipes
Deforestation
D. What are the Risk Factors for each event?

## Slide 19
Water Source | Water Distribution System
Drinking Water Supply flow is uncontrolled/ Drought
Variable/ Low water levels
Damaged Collection Structures
Leaks
Blocked Piping
D. What are the Risk Factors for each event?

## Slide 20
Disaster/ Climate Change Effects
Low level Flood Plain
(Flooding)
Base of Slope
(Landslide)
Earthquake Zone
(Earthquake)
Near the shoreline
(Tsunami/King Tide)
Near River
(Flooding)
Near Gully
(Subsidence)
D. What are the Risk Factors for each event?

## Slide 21
Fencing around a source
Mesh Inlet Screen
Filters – Gravel or Sand
E. Control Measures – Bacteria/Chemical

## Slide 22
Spring Box
Covering a source
Diversion Ditch
Overflow Pipe
E. Control Measures – Bacteria/Physical

## Slide 23
Solid Base
Sealed Cover
Clean with no leaks
E. Control Measures – Bacteria/Physical

## Slide 24
Min Head Device e.g. Dam
Overflow Pipes
Pressure Break Box
E. Control Measures – Controlling Flow

## Slide 25
Storage and Settlement
Filters
First Flush Rainwater
E. Control Measures – Treating Water

## Slide 26
Establish drinking water protection zones (Fencing)
Reduce use of fertilisers near catchments
For surface: Install and maintain screens and sediment traps
D&E. Best Practice – Surface Sources

## Slide 27
Protect source against run off flows (Diversion Ditch)
Keep toilets and septic tanks 30m away from source
For spring: Construct a safe collection chamber
Prevent roaming of animals near the source (Fence)
D&E. Best Practice – Spring Sources

## Slide 28
Regular cleaning, inspection and maintenance of storage
Keep collection roofs clean
Repair leaks and cracks to avoid contaminant ingress
Keep Collection areas clean
Put inlet screens on tanks
D&E. Best Practice – Rainwater Collection

## Slide 29
With so many Events how can we identify Risk Factors and Control Measures on our system?
Main Tool for Risk Factor and Control Measure Identification
SANITARY SURVEYS
D&E. How to identify risks and control measures

## Slide 30
Supply/Storage Hazards and Control Measures
1 Group perform Sanitary Survey for the Water Source
1/2/3… Group/s perform Sanitary Surveys on Distribution Points
COMPLETE RISK FACTORS AND CURRENT CONTROL MEASURES COLUMN ON TEMPLATE
Distribution Hazards and Control Measures
Present back to group on risk factors and control measures for the water system
Tick the relevant boxes. Are there any more that need listing?
Identifying Risks and Control Measures - Exercise

## Slide 31
We have 3 levels of Risk
HIGH
MEDIUM
LOW
What this means
Action needed
The system is not secure and the chances of contamination are high
Improvements needed now
The system has some protection but still could get contaminated
Improvements are needed but not immediately
The system is well protected with a low chance of contamination
No action required but must be monitored
F. Evaluating/ Ranking Risk

## Slide 32
How do we calculate our level of Risk?
HIGH
MEDIUM
LOW
Hazard
Hazard
Hazards present
Control Measure
Control Measure
No Control Measures
Hazard
Hazard
No Hazards
Control Measure
Control Measure
Control Measures present
Hazard
Hazard
Hazards present
Control Measure
Control Measure
Control Measures present
Hazard
Hazard
No Hazards
Control Measure
Control Measure
No Control Measures
AND
AND
F. Evaluating/ Ranking Risk

## Slide 33
COMPLETE RISK COLUMN ON TEMPLATE
Look again at your answers for your water system
Calculate the risk for each Hazard Event on each part of your water system
Present back to the group on the level of risk within the water system
Evaluating/ Ranking Risk – Exercise

## Slide 34
HAZARD
Drinking Water Supply
Control Measure
Control Measure
Control Measure
The more barriers we have the better we can minimise the risk to the supply
So how do we improve?
Why improve?
G. Improve/ Manage Risk

## Slide 35
1. Decrease the number of Hazards/ Risk Factors
We can improve/ manage risk in 2 ways:
Hazard
Control Measure
Hazard
Hazard
Hazard
Hazard
Hazard
Hazard
Hazard
Control Measure
2. Increase the number of Control Measures
Control Measure
Control Measure
Control Measure
Control Measure
Control Measure
G. Improve/ Manage Risk

## Slide 36
How can we decide what improvements are needed?
DECISION FLOW DIAGRAMS
OR
OUR OWN IDEAS
G. Improvements Required?

## Slide 37
COMPLETE IMPROVEMENTS COLUMN ON TEMPLATE
Run Flow Diagram (Decision Diagram) exercise using posters
Each group to tick required improvements or list additional or more relevant actions
Identifying Improvements – Exercise

## Slide 38
End of Session