## Slide 1
Drinking Water Safety & Security Planning
Part 2 Implementing DWSSP
Planning for Adequate Sanitation
DWSSP Programme

## Slide 2
Water Security is complicated, but we believe a Water Secure community has 3 things:
Has reliable access to enough water quantity of good enough quality for drinking and human well being inclusive of sanitation and hygiene
Has adequate sanitation provision, and collects and treats waste water in order to protect humans and the environment from pollution
The ability to cope with uncertainties and risks of water-related hazards, for normal operation, disaster scenarios and long term changes
What is a Water Secure community?

## Slide 3
DWSSP Programme

## Slide 4
Good Sanitation
Clean Water
Hygiene
Hygiene
Adequate Sanitation – First defence

## Slide 5
Human Waste
Hygienically preventing contact of waste to humans via the following
Through the food chain
Through the environment and drinking water
What do we want Sanitation to do?

## Slide 6
ADEQUATE SANITATION is where the proper facilities exist for safe and dignified disposal of human faeces and urine. Human behaviour and practices are also key to this.
1. Good Shelter Structure
2. Good Ventilation
3. Clean Toilet Pan
4-6. Waste is stored or disposed of safely
7. Hand Washing is available
7
What is adequate sanitation?

## Slide 7
Toilets – Common Types
Dry Types
Compost Toilets or Pit Latrines
No Water Used
Good for saving water in village but needs maintenance
Types of Sanitation

## Slide 8
Toilets – Common Types
Wet Types
Pour Flush Toilets
or Flush Toilets
Water Used
Easier to clean/maintain but does require water
Types of Sanitation

## Slide 9
Different Types of Waste Water
Grey Water
Waste Water from washing, laundry and cooking
NO HUMAN WASTE
Black Water
Waste Water from toilets
WITH HUMAN WASTE
Waste Water Types

## Slide 10
How much black water do we generate?
per
per
N Litres
2 litres – Dry Toilet
10 litres – Wet Toilet
1 Person
1 Day
All Black Water Should be Treated
Waste Water Amount

## Slide 11
How do we calculate?
N Litres
Population Number
Total Number of Litres Per Day
x
=
EXERCISE – Calculate requirements for community now in groups (10mins). Discuss waste storage requirements.
Waste Water Amount

## Slide 12
Toilets – How many are required?
Requirements
Are within 250m of dwellings (2-3mins)
Household to
Toilet Ratio = 1:1
How many toilets are adequate?

## Slide 13
How good are your toilets?
The standard of the current toilets is important when assessing water security
Main Tool for Assessing Toilet Standards?
SANITARY SURVEYS
What is an adequate toilet?

## Slide 14
Waste System Requirements - Exercise
Toilets
Each Group fill out the number of toilets they have in their community
What is the ratio of HH to Toilets? Fill in Section 2
Condition of Toilets
1/2/3… Group/s perform Sanitary Survey for all the toilets in the village where possible. What is the condition? How many need upgrading?
COLLATE ALL EXERCISE INFORMATION. COMPLETE SECTION 3C IN DWSSP

## Slide 15
Waste System Design
What are the key parts of a waste system?
Source
Storage and Primary Treatment
Secondary Treatment
Outlet to Environment
FOCUS WILL BE TOILETS

## Slide 16
Waste System Design
How do we design the system?
DECISION FLOW DIAGRAMS

## Slide 17
Waste System Design – Toilets
Toilet Options – Compost Toilet
Dry toilet that uses no water for flushing. All waste is captured within a closed chamber
Advantages:
Almost no water needed
Does not pollute groundwater
Can be located anywhere
Compost can be used on soil for agriculture
Clean and hygienic

## Slide 18
Waste System Design – Toilets
Toilet Options – Compost Toilet continued
Disadvantages:
Organic matter (e.g. grass) must be regularly collected and stored in the toilet
Users need to understand and control the addition of grass
Can be expensive
Users have to empty waste from collection chamber twice a year
Access can be difficult

## Slide 19
Waste System Design – Toilets
Toilet Options – Pour Flush Toilet
Like a regular flush toilet only water is poured by the user using a bucket
Advantages:
Low cost
Can control flies and mosquitos
Absence of smell
Low water use
Can be upgraded easily e.g. connected to sewer

## Slide 20
Waste System Design – Toilets
Toilet Options – Pour Flush Toilet continued
Disadvantages:
Reliable water supply needed
Potential for groundwater pollution
Need to move toilet if new pit is dug

## Slide 21
Waste System Design – Toilets
Toilet Options – Flush Toilet with Septic Tank
Toilet where waste is flushed into sealed septic tank
Advantages:
Convenience and status
No smell or insects
Can be located in a house
Easy to Clean

## Slide 22
Waste System Design – Toilets
Toilet Options – Flush Toilet with Septic Tank cont
Can pollute groundwater if high water table or outflow is poorly designed
Needs expensive septic tank collection occasionally
High cost to maintain
Disadvantages:
Expensive
Needs reliable and adequate water supply
Not suitable if small area for outflow

## Slide 23
Are there enough toilets in the community?
Use Toilet/HH Ratio (Should be 1)
Use People/Septic Tank Ratio
Max Distance of 250m to HH
Install New Toilets
Do existing toilets need upgrading?
NO
YES
Are there enough toilets in the community?
Use Sections 1 & 2 data to answer
IF NO SEE “INSTALL NEW TOILETS” MATRIX
Waste System Design – Toilets

## Slide 24
Identify number of toilets requireD
Is water supply adequate?
Select toilet type through decision tree
Fill in section 3C
Waste System Design – Toilets

## Slide 25
Do existing toilets need upgrading?
Toilet Sanitary Survey
Upgrade Toilets
YES
SYSTEM SECURE
NO
Do existing toilets need upgrading?
Use Sanitary Survey data to answer
IF YES SEE “UPGRADE TOILETS” MATRIX
Waste System Design – Toilets

## Slide 26
Identify how many toilets need upgrading
Audit and list requirements
Mark relevant upgrades on community map
WHEN FINISHED – SANITATION PLANNING IS COMPLETE
Waste System Design – Toilets
Fill in section 3C

## Slide 27
End of Session